## Slide 1: SpaceX Senior FPGA Engineer Interview Presentation: Simple Uart
Frank Bruno

## Slide 2: Background
20+ years digital design/ architecture
  10+ ASICs
    High speed/ large gate count
    Low power
  10+ FPGAs
    Altera/ Xilinx/Lattice/Actel(Microsemi)
    Low cost/ Low power
    High speed/ large gate count
Networking/ Graphics/ SDR/ Defense

## Slide 3: Definition
Support all standard baud rates up to 57600 baud
7x oversampling
Data/control bit determined by voting on the middle 3 samples
1 start bit, 13 data bits, programmable parity and one stop bit
8 entry FIFO buffer for RX and TX
8-bit CPU bus interface
RTS/CTS flow-control

## Slide 4: Design Procedure
UART
  standard component
    Existing open core or vendor library.
New design
  Show process
  Design different enough
    13 data bits
    7x oversampling
    Fifo Depth
  Software reuse – CPU interface

## Slide 5: Clocking choices
Create UART clock
  Maximum clock rate due to oversampling: 7x57600 = 403.2Khz.
  Extra clock domain
  Closer to necessary frequency, larger the potential error and bit slip or more precise clock.
Create clock enable
  Run at clock enable @ frequency approximating 7x oversampled baud rate

## Slide 6: Determine clocking requirements
Support all standard baud rates up to 57600
Utilize higher frequency clock (100Mhz)
  Divisor {HI, LO} = (clock frequency / (baud rate * 7))-1
Create programmable clock enable to mimic slower clock
Lower baud rate support but lowering system clock
Baud | HI | LO | %ERROR
300 | 8'hB9 | 8’hFF | -0.006382%
1200 | 8'h2E | 8’h7F | -0.006325%
2400 | 8'h17 | 8’h3F | -0.00625%
4800 | 8'h0B | 8’h9F | -0.0061%
9600 | 8'h05 | 8’hCF | -0.0058%
14400 | 8'h03 | 8'hDF | -0.0055%
19200 | 8'h02 | 8'hE7 | -0.0052%
28800 | 8'h01 | 8’hEF | -0.0046%
38400 | 8'h01 | 8’h73 | -0.004%
57600 | 8'h00 | 8'hF7 | -0.0028%
Speedtest.h

## Slide 7: Protocol
RTS/CTS flow-control
  TX: Check CTSn to make sure RX is ready (0=READY)
  RX: RTSn shows RX FIFO full 0 = Not full, 1 = full
Programmable Parity
  None, Even, Odd, (Stuck at level support not entirely tested)
7x Oversampling with voting:
  Helps with bit slip
  Allows larger rate mismatch
  Voting strategy gives us 2/7 baud clock of margin
  Noisy environment
    2 out of 3 center signal

## Slide 8: Architecture
RX/TX Baud Clock Enable Gen
RX/ TX SM
CPU Interface
TX FIFO
RX FIFO
uart_rx
uart_tx
ctsn
rtsn
sys_clk
sys_rstn
cpu_csn
cpu_rdwrn
cpu_addr
cpu_din
cpu_valid
cpu_dout
cpu_int

## Slide 9: CPU interface
Custom or 16550
  Custom was my first choice
  Easier testing
16550 is industry standard with existing drivers
  Re-using this interface requires only minor changes
    2x Write Data or 2X read data
    Minor changes for unused registers and signaling
    FIFO levels are 8 values
  Simple 8 bit interface for reading and writing.
    Chip Select
    3 bit address for 16 registers
    Rd/Wrn
    8 bit data in and out
    Interrupts
      Not asked for, but UART is very slow relative to system
      Avoid tying up CPU

## Slide 10: FIFO
Due to my design choices, I will utilize a synchronous FIFO.
  Don’t need to worry about clock crossing
  Coded by hand rather than generating a core
If we were running independent clocks, we would need to use an asynchronous FIFO.
  Example included in appendix with discussion on FIFO clock crossing

## Slide 11: Environment
Uart (Root)
  Rtl (Verilog source code)
  Stim (Testbench and build files)
  Sim
    Runsim –a (run all tests under ./tests)
    Runsim –f ./tests/speedtest.h (run single test)
      Supports .h and .h.gz files
    Produces “passed” and “failed” files showing test status
  Sim/tests
    Self checking tests
    If a test fails, it sets the test_failed flag
  Vivado (FPGA build directory)

## Slide 12: Testing
CPU Register R/W test
Simple Internal loopback test
  Parity modes (none, Even, Odd)
Simple External loopback test
Rate performance testing
Two UART TX/ RX testing
  Pass 128 values from UART->UART using RX polling
  TX/ RX FIFO interrupt testing
Parity error mismatch to test parity errors on RX
Speed Mismatch and error detection

## Slide 13: Self checking tests

## Slide 14: 2x UART Simulation

## Slide 15: Design Changes
Rate mismatch test showed problems
  Change RX to terminate after Stop bit voting to help with slow sampling
Separate RX baud clock enable generation
  Reset generation when RX starts

## Slide 16: Thank You!

## Slide 17: Appendix: Asynchronous - Gray Code for FIFO levels
Crossing mismatched clock domains
Fifo level is a difference between read and write pointers
  Read and Write addresses:
    Gray coded
    Registered on own clock domain
    2x Registered on opposite clock domain
      Ensures a single bit transition.
    Convert back to binary
      Take the difference to generate Full, Almost Full, Almost Empty and Empty flags